A method to simulate solute transport
Andriy Bun, Timo Heimovaara
# Abstract
Text
# Model
The described method combines properties of both marker-in-cell technique (Gerya, 2009)⁠ and finite cell method (Sun, 1999)⁠. Its basic idea is to use Lagrangian advecting points (marker, tracers or particles) and combine it with an immobile Eulerian grid. In this approach properties are initially distributed on a number of Lagrangian points that are advected according to a given/computed velocity field. The advected properties (e.g. concentrations) are then interpolated from displaced Lagrangian points to the eulerian grid (Gerya, 2009)⁠.
Describe modifications to marker-in-cell method:
- markers with volume / mass;
- interpolation of velocity field.
- subgrid diffusion term calculation to keep mass balance correct;

# Validation
In order to validate the described method, it was tested against a number of analytical solutions. Convection-diffusion equation (CDE) is a commonly accepted model for solute transport. Without sources/sinks this equation has a form:
partial over {partial t} C(x, t) = nabla (D cdot nabla C(x, t)) - v cdot nabla C(x, t).	(1)

We consider test cases with initial concentration defined as follows:
C(x,0)= ~ binom{C_0, 0<=x<=l;}{0, otherwise;}	(2)

and boundary condition:
partial over {partial t} cdot C(infinity,t)=0.	(3)

Equation (1) with initial and boundary conditions (2) and (3) respectively has following analytical solution (modified from (Jost, 1960)⁠):
C(x, t) = - {{C_{0}} over {2}} cdot erf left ( {-x + v cdot t} over {2 cdot sqrt(D cdot t)} right ) + {{C_{0}} over {2}} cdot erf left( {-x + l + v cdot t} over {2 cdot sqrt(D cdot t)} right).	(4)

This solution contemplates homogeneous diffusion coefficient and constant velocity homogeneous over the entire domain. Therefore for validation a corresponding system was initialized with initial concentration defined as in (2), homogeneous properties over the entire domain and constant homogeneous flux.
For validation purposes the length of column l was set to 1 meter. Analytical solution (4) is valid on an infinite domain. Therefore in order to approximate behavior of solute on an infinite domain a system was extended by 3 extra meters on either side. Test cases considered:
No influx case v=0 :
  1. Due to no flux condition, the transport of solutes is governed only by diffusion.

Fig. 1. Comparison of simulation results (narrow lines marked with crosses) vs. analytical solution (solid bold lines).
Figure 1 shows that the applied method is very accurate and there is almost no difference between numerical simulation and analytical solutions for a selected case.
  1. In real physical systems however it is likely that solute can't diffuse outside of column x<0 . In this case symmetric reflection must be implemented at x=0 . This means that particles of solute that reach zero coordinate do not move outside of domain but are reflected backwards. Hence the solution consists of two parts (Jost, 1960)⁠:
C_ref(x, t) = C(x, t) + C(-x, t).	(5)

Results of simulating for the mentioned case are shown in figure 2.

Fig. 2. Comparison of simulation results (narrow lines marked with crosses) vs. analytical solution (solid bold lines).
1. Another cases considered involved constant flux:
  1. Boundary concentration is defined as C(0, t) = 0 . Diffusion coefficient D is set to zero. In this case advection will be the only process present and hence the sharp edges of concentration profile should be preserved. This is not possible to achieve with finite difference methods (Gerya, 2009)⁠ due to numerical diffusion. Figure 3 shows that the described method deals with the problem very well.

Fig. 3. Comparison of simulation results (narrow lines marked with crosses) vs. analytical solution (solid bold lines).
  1. Boundary concentration is defined as C(0, t) = 0 . Figure 4 shows the results of simulating solute flux for such a case in comparison with analytical solution.

Fig. 4. Comparison of simulation results (narrow lines marked with crosses) vs. analytical solution (solid bold lines).
  1. Now consider zero initial concentration C(x, 0) = 0 and instantaneous injection of solute at time t = 0,`C(0, t)=%delta(t). Analytical solution for CDE with such initial and boundary conditions is defined in (Jury & Roth, 1990)
C(x, t) = x over {2 cdot sqrt{%pi cdot d cdot t ^ 3} } cdot {exp left(-(x - v cdot t) ^ 2 over {4 cdot d cdot t} right)}.	(6)

Fig. 5. Comparison of simulation results (narrow lines marked with crosses) vs. analytical solution (solid bold lines).
Figure 5 illustrates that for the case of instantaneous influx of solute some difference exists between for shallow depths. This is most likely due to the impossibility to numerically simulate Dirac delta function for boundary concentrations. However the concentrations tend to analytical solution with increasing depths where the concentrations are smoothed out.
# Simulating 2-phase solute flux

# References